## Slide 1: How does the CPU work?
CPU’s program counter (PC) register has address i of the first instruction
Control circuits “fetch” the contents of the location at that address
The instruction is then “decoded” and executed
During execution of each instruction, PC register is incremented by 4 (assuming RISC CPU and 4 byte word size) …
But *how* exactly are these things done?
Here, we see a VERY simple architecture that shows how!
Real architectures work the same way, fundamentally, though; all the basic concepts are the same, but real CPUs add a lot of complexity on top of these basic concepts!

## Slide 2: A very simple (accumulator) machine
8-bit words, 5-bit address (so 32 byte/word memory), 3-bit op-code, so, 8 different instructions possible)
Processor has only ONE general purpose register, called an accumulator (earliest processors were usually like this!)
Instructions and op-codes (LOAD is read memory; STORE is write memory):
  In machine language, op-code is in bits 0 – 2 (starting with leftmost bit) and address is in bits 3 – 7 (all instructions 8 bits, or 1 word in length):
  Example code for C = A*B + C*D A (label for var) in word at 20, B in 21, C in 22, D in 23; word at 30 (E) is used for temporary storage
  100 10100 LOAD A 100 10110 LOAD C 010 10101 MUL B 010 10111 MUL D 101 11110 STORE E 000 11110 STORE C 100 10110 LOAD C
ADD 000 | SUB 001 | MUL 010 | DIV 011
LOAD 100 | STORE 101 |  | 

## Slide 3: Notes on simple architecture
Word size is 1 byte
Notice all instructions are 1 word long (8 bits or 1 byte)
Each instruction in machine language has 2 parts or fields: (1) op code (leftmost 3 bits) and (2) memory address (rightmost 5 bits) for memory operand
All instructions read or write the accumulator (only register) and also read or write a memory word
8 instructions possible (because 3-bit op code) but only 6 instructions implemented (only 6 op codes used)
NOTICE: Only sequential execution (no call/return or branch/jump instructions)! NO REAL PROCESSOR EVER HAD ONLY SEQUENTIAL EXECUTION!!!!!

## Slide 4: Internal Structure of Simple CPU
Bus
MAR
MDR
2 → 1
MUX
INC
PC
ACC
ALU
2 → 1
MUX
Decode
Timing
and
Control
IR
OP
Addr

## Slide 5: Internal Structure of Simple CPU
Bus
This bus is internal to the CPU (inside the CPU) .There is a separate bus (memory bus) from the memory to MAR and MDR registers to communicate with memory

## Slide 6
Bus
MAR
MDR
MAR is Memory Address Register MDR is Memory Data Register
To read a word in memory, the CPU must put the address of the memory word in the MAR, set the “read enable” bit, and wait for a certain no. of clock cycles (delay for access); at the end of that, the value at that memory address will appear in MDR
To write a word to memory, the CPU must put the address of the memory word in the MAR and the value to be written in MDR; set the “write enable” bit; wait for a certain no. of clock cycles (delay for access), and at that point, the value is in memory at the address specified.

## Slide 7
Bus
MAR
MDR
2 → 1
MUX
INC
PC
PC is the program counter. INC is a simple circuit whose output is one greater than its input.
The MUX is a multiplexor which will output one of its two inputs, depending on the value of a control signal (not shown); this allows for normal control flow and branches, which are not implemented, but could be.

## Slide 8
Bus
MAR
MDR
2 → 1
MUX
INC
PC
ACC
ALU
2 → 1
MUX
ALU is the arithmetic/logic unit and does all the math
ACC is the accumulator (it is the only general purpose register).
It can be loaded with a value from the ALU or the bus; the value in it can be used as an input to ALU or copied into MDR (why? when?)

## Slide 9: Only sequential execution
Notice that the PC is always incremented by 1 (because all instructions are 1-byte long).
There is no non-sequential execution, using an instruction such as call/ret or branch/jump (but they could be implemented)
Very simple instruction sequencing (again, only sequential) – after an instruction, the next instruction in memory is executed – no real machine was ever this simple (the sequential execution only limitation makes the machine not very useful)!

## Slide 10
Bus
MAR
MDR
2 → 1
MUX
INC
PC
ACC
ALU
2 → 1
MUX
Decode
Timing
and
Control
(TAC)
IR
OP
Addr
IR (instruction reg.) contains the instruction being executed.
The decoder splits it into the address and operation to be performed (Decode unit does this).
Timing and control generates the correct control signals and, in effect, runs the whole show

## Slide 11: “Operations” on next slide
“Operations” on the next slide are things that must be done (data movement or loading a register) as part of executing various instructions
Not all operations are done for each kind of instruction
Various operations may be done in a single clock cycle (see below)
NOTE: “bus” in the description of an operation means the internal CPU bus, not the memory bus.

## Slide 12
“Timing and control” (TAC) generates a set of “control signals” that essentially control what happens. Key inputs to TAC: clock, condition signals
…
Condition
signals
Next-state
Current-state
(register)
Clock
Control
Control signals
Operation
Number Operation
0 Acc → bus
1 load Acc
2 PC → bus
3 load PC
4 load IR
5 load MAR
6 MDR → bus
7 load MDR
Operation
Number Operation
8 ALU ¬ Acc
9 INC → PC
10 ALU operation
11 ALU operation
12 Addr → bus
13 CS
14 R/W
Key idea:
At each clock cycle,
current state is updated to the appropriate next state
and a new set of ctrl signals generated

## Slide 13: More on Control Signals
We will not look at the control signals in detail.
What is important to understand is what kinds of things the control signals (generated by the TAC unit) do.
They determine, for example, which lines (bus lines and lines which connect units to bus lines) will allow signals to pass (are “open”; by ANDing 1 with bits on line), and which will not allow signals to pass (are “closed”; by ANDing 0 with bits on line)
They also determine the control signals that will be input to MUX units (to select the correct input to pass to the output of the MUX)
We will discuss examples of how this works below.

## Slide 14: Clock Cycles Per Instruction
On the next slide, the changes in each state (each numbered box) take one clock cycle per box
Different instructions require the actions in different sequences of boxes, although all instructions require the changes in boxes 0, 1, 2, and 3
From this, it can be seen that each instruction takes 6 clock cycles (4 for fetch/decode, and 2 for execution)
CS is “condition signals” and R/W is “read/write”
CS (condition signals) consist of current state (at least) and perhaps other signals (see below)

## Slide 15: Finally: How the CPU works/states
PC → bus
load MAR
INC → PC
load PC
0
CS, R/W
1
2
3
4
5
6
8
7
MDR → bus
load IR
Addr → bus
load MAR
CS
OP=store
OP=load
Yes
Yes
No
No
ACC → bus
load MDR
MDR → bus
load ACC
CS, R/W
MDR → bus
ALU ¬ ACC
ALU op
load ACC
States 0,1,2, 3: Fetch
Rest: Decode, execute

## Slide 16: Operations again
All instructions require the operations shown in states 0, 1, 2, and 3
The remaining operations depend on the instruction:
Store: 4, 5
Load: 6, 7
ALU: 6, 8
KEY POINT: Since the operations in each state require 1 clock cycle to complete, all instructions take multiple clock cycles (6 clock cycles in this design); this is true of all real processors, including ones we have today.

## Slide 17
“Timing and control” (TAC) generates a set of “control signals” that essentially control what happens. Key inputs to TAC: clock, condition signals
…
Condition
signals
Next-state
Current-state
(register)
Clock
Control
Control signals
Number Operation
0 Acc → bus
1 load Acc
2 PC → bus
3 load PC
4 load IR
5 load MAR
6 MDR → bus
7 load MDR
Number Operation
8 ALU ¬ Acc
9 INC → PC
10 ALU operation
11 ALU operation
12 Addr → bus
13 CS
14 R/W
Key idea:
At each clock cycle,
current state is updated to the appropriate next state
and a new set of ctrls signals generated

## Slide 18: Interrupts and non-sequential control flow
As the prior slide says, if we wanted to handle interrupts, an interrupt line would have to be input to the next state unit, to change the next state unit appropriately if an interrupt occurs.
Call, return, and jump/branch instructions would also require inputs to the next state unit, and other changes as well (such as a way to write an address from an instruction (the address of the label in the instruction) to the PC)

## Slide 19: Improving Performance
Over time, various ideas have been used to significantly improve performance of our system hardware
Here, we look at three of the most significant ones:
  Memory hierarchy/caching
  Pipelining
  Multicore CPUs

## Slide 20: Improving Performance (cont)
Problem: Speed mismatch between CPU and memory
Memory *can* be fast but then becomes very expensive (because very fast memory technology costs about 10 times as much per byte); OUR SYSTEMS WOULD COST WAAAAAAAY MORE WITH FAST MAIN MEMORY!!!!! (imagine needing a loan similar to a house/car loan to buy a computer system :-( )
Solution: Memory hierarchy (levels of memory): (cheaper, slower memory as you go down levels in the list)
Hierarchy levels (highest to lowest)
  See next slide

## Slide 21: Improving Performance
Hierarchy levels (highest to lowest)
  CPU Registers (very fast memory - SRAM)
  Cache (Level 1, Level 2, …) (also very fast memory - SRAM)
  Main memory (often called RAM: Random Access Memory): Note that term “memory” alone refers to RAM; this is slower memory – DRAM (10 to 20 times slower!!!!!)
  Disk/SSD, …
  Flash cards, tapes etc.

## Slide 22: Analogy – "Old-fashioned" Library Research
In the “old” days (when I was your age!), research was done with printed books and articles
If you wanted to write a research paper, you would go to the library, look for books and articles on your topic, and go and get them from the “stacks” (shelves with printed books and lournals), by taking the elevator to a higher floor and going out and finding them
If you found 50 books and articles, you could not keep all of them on your small library desk at one time, so you would only bring the ones you were using for the part of your paper you are currently writing (because that's all you have space for on your small desk)
Others you would leave in the stacks till you were ready to use them
The stacks are like main memory (huge, but slow retrieval time), and the small desk is like cache (small space, but fast retrieval time)

## Slide 23: Memory hierachy (contd)
Key requirement: Data that CPU needs next/soon must be as high up in the hierarchy as possible, for fast access (otherwise, CPU has to wait); therefore, this data (or instruction) should be in a register or cache.
Important concept: Locality of reference
Temporal locality: A recently executed instruction (or recently accessed data) is likely to be executed (or accessed) again soon
Spatial locality: Instructions (or data) near a recently executed instruction (or recently accessed data) are likely to be executed (or accessed) soon

## Slide 24: CPU cache
All modern CPUs have cache storage
The cache access is much faster because:
  It is on the same chip as the CPU, and
  It uses fast memory (SRAM), so the read/write access time is very fast (one clock cycle)
Whenever data/instructions are moved from memory to CPU, they are moved into the cache (or, if written back to memory, written from the cache)
An Intel i7 has about 7 MB of cache, so it is less than 0.1% (one-tenth of 1 per cent – 1/1000) the size of main memory (RAM), but it still improves performance TREMENDOUSLY

## Slide 25: Cache and Main Memory
CPU
Cache
Main
Memory
When a Read is received and the word is not in the cache, a block of words containing that word is transferred to cache (one word at a time)
Locality of ref. means future requests can probably be met by the cache
CPU doesn’t worry about these details … the circuitry in the cache handles these transfers

## Slide 26: Remember….
The cache is only a tiny fraction of the size of the main memory/RAM (about 0.1 percent)
That means only a small percentage of what is in memory can be in the cache at any given time
What is in the cache is only a copy of something in memory (instruction or data); the copy in memory is also still there
As we said above, when data/instructions are moved from memory to the cache, they are moved a block at a time (see below for discussion of block size)

## Slide 27: Cache structure & operation
Organized as a collection of blocks
  Example: Cache of 128 blocks, 16 bytes/block (so 128 X 16 = 2048 byte cache capacity)
  Mem: 64K bytes, 16 bit addr: 4K blocks (because 16 bytes per block); notice cache block and memory block must have the same size.
  Direct-mapping approach: Block j of mem. → Cache bl. j mod 128 (because cache has 128 blocks) So blocks 0, 128, 256, … of mem. will all map to cache block 0; etc.
  In direct-mapping approach, any block of memory can only go in one specific cache block (no choice on where to put it)
  Mem. addr.: 5 tag bits + 7 block bits + 4 word bits
  Division of address explained on next slide

## Slide 28: Division of Memory Address for Cache
Explanation of how memory address is divided into bit fields
(Reminder) Mem. addr.: 5 tag bits + 7 block bits
+ 4 byte bits
  Tag bits → Which of mem. block 0, 128, …?
  Block bits → the relevant cache block Word bits → which word in block
  Whenever there is an access to memory by CPU, address is divided this way
  Explanation: 7 block bits because cache has 2^7 blocks; 4 byte bits because 2^4 bytes per block; tag bits are remaining (most significant) bits

## Slide 29: Address Fields (Parts)
Address fields for above example
Part | Tag (5 bits) | Block | Byte
Number of bits | 5 bits | 7 bits | 4 bits

## Slide 30: Cache structure & op (contd)
When a block (16 bytes) of memory is stored in the corresponding cache block, the cache also stores the tag bits of that mem. block (but no other bits from address)
When CPU asks for a word of memory:
  Cache does not look at 4 least significant bits of address (byte bits), but only 12 most significant
  Mods those 12 bits by 128 to get the cache block (block 0, 1, 2, … 127)
  Cache compares the leftmost 5 bits of addr. with tag bits stored with that cache block
  If bits match, there is a cache hit (the instruction/data is in the cache; now the least significant 4 bits are used to get the correct word, starting at that byte from cache), and the CPU can use copy in cache; if tag bits don't match, there's a cache miss.

## Slide 31: Direct-mapped cache
The big advantage of a direct-mapped cache is that it can be searched extremely fast (because only one place to look in cache) for any address in memory
The disadvantage is that if a program is frequently using two or more blocks in memory that all must go in the same cache block, only one of them can be in the cache at a time (so they end up getting swapped in and out of the cache a lot); this is called a collision (multiple blocks that must go in the same cache block).
There are other kinds of caches which improve this, but as you should guess, they are more expensive – they cost more to implement (there’s “no free lunch”)

## Slide 32: Cache Hit Rate
The percentage of memory accesses by the CPU that hit in the cache is called the hit rate
When the CPU tries to access instructions or data not in the cache, this is called a cache miss
Hit rates in the 90% range are common in programs (though it depends on the type of software), so a cache can improve average memory access time (and performance) a lot
For this reason, caches are universal in modern systems (and all systems actually use multiple caches for different purposes; more on this later)

## Slide 33: Cache structure & op (contd)
But what if the memory access by the CPU is a write op?
Need to update copy of data (but not instruction – instructions cannot be written) in main mem. as well. 2 different approaches are used:
  Write-through protocol: Update both the value in cache and in memory
  Write-back protocol: Update only the cache
  location but set cache block’s dirty bit to 1 (dirty bit is used to track whether cache block has been written/modified since it was brought into the cache)

## Slide 34: Cache structure & op (contd)
What if the word is not in the cache (a cache miss)?
Need to read the entire block of memory that contains that word, i.e., based on first 12 bits of address, into the right cache block
  But first: check if dirty bit of that cache block is 1 (if write-back is being used) and, if so, write it back to memory before doing the above to replace the cache block
  This can lead to poor performance -- depending on the degree of spatial/temporal locality of reference

## Slide 35: Cache structure & op (contd)
Associative-mapping approach:
  A main-memory block may be placed in any cache block
  Each cache block has a *12 bit* tag (12 msbs of address) that identifies which mem. block is currently mapped to it
  When an address is received from CPU, the cache compares the first 12 bits with the tag of each cache block to see if there is a match
  That can be done quite fast (in parallel; that is, compare 12 bits with all tags at the same time), BUT, as we said before, this makes the cache much more expensive

## Slide 36: Cache structure & op (contd)
For anything other than direct-mapping need suitable replacement algorithm; that is, if all the spots in the cache are full, and we want to bring in a new block, which block do we replace?
Widely used replacement algorithm in systems with associative caches: replace least recently used (LRU) block
Even small caches are useful for improving performance significantly (as we saw above, typical cache size is less than 0.1% of main memory size, even in high performance CPUs such as Intel i7)

## Slide 37: Cache structure & op (contd)
Good measure of effectiveness: hit rate and miss rate
These can depend on the program being executed
Compilers try to produce code to ensure high hit rates (high percentage of cache accesses with data found in the cache)
Cache structure can also be tweaked: e.g., have separate “instruction cache” and “data cache”

## Slide 38: Pipelining introduction
As we saw above, in all processors, even simple ones, each instruction requires the execution of multiple steps or stages (in order), each of which takes 1 clock cycle.
This means each instruction takes multiple clock cycles.
Decades ago, some bright computer architects got the idea of executing different stages of multiple consecutive instructions at the same time, in order to improve performance.
This way of executing multiple instructions at the same time is called pipelining, and it is used in all processors today.
As we will see, pipelining can improve performance tremendously (that is why it is universal today)!

## Slide 39: Improving performance: Pipelining
Key idea: Simultaneously perform different stages of consecutive instructions, so execute multiple instructions at the same time: F(etch), D(ecode), E(xec), W(rite) [So, 4 stages here]
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
I1 | F1 | D1 | E1 | W1 |  |  | 
I2 |  | F2 | D2 | E2 | W2 |  | 
I3 |  |  | F3 | D3 | E3 | W3 | 
I4 |  |  |  | F4 | D4 | E4 | W4
Need buffers (data storage elements) between stages to hold the data related to execution of each stage.

## Slide 40: Notes on pipelining
Notice on the prior slide that it is not till clock cycle 4 that 4 different instructions are being executed simultaneously; the first 3 cycles are required to "load" the pipeline (get 1 instruction into each stage)
If a large number of instructions will be executed (always true in programs), the load time is negligible, and can be ignored
After the pipeline is loaded, notice that 1 instruction per clock cycle completes execution
Therefore, if we ignore the load time, we can say that pipelining allows execution of 1 instruction per clock cycle
Without a pipeline, 4 clock cycles would be required to complete each instruction; thus, pipelining offers an improvement in performance of 4 times in this example (the number of pipeline stages)

## Slide 41: Performance Improvement
Why does pipelining improve performance?
  Once the pipeline is “loaded,” on average, one instruction completes every clock cycle.
  In non-pipelined processors, instructions generally take multiple clock cycles to complete (4 cycles typically, in the model used here, because only one stage for one instruction can be completed per clock cycle).
So how much of a speed-up (maximum) does a pipelined processor offer?
Will a longer pipeline (more stages) be better, worse, or no different in terms of performance?
Note: Intel Pentium 4 (an old processor) had a 20 stage pipeline. 20 stages (or more) is quite typical of CPUs today, but the whole story is rather complex….

## Slide 42: Pipelining - Improvement
In real pipelined processors, we cannot quite reach one instruction completing per clock cycle, but we can usually get close (0.9 instructions per clock cycle average is quite reasonable to achieve).
If 0.9 instructions complete per clock cycle on average, how much of a performance improvement do we get for a 20 stage pipeline?

## Slide 43: Pipelining (contd)
Need buffers (memory/storage) between stages
Write
results
Fetch
Instruction
Decode ins
& Fetch
operands
Execute
operation
B3
B2
B1
During clock cycle 4 (see slide 38 above):
Buffer B1 holds I3 which was fetched in cycle 3 and is being decoded
B2 holds both the source operands for I2 and specification of operation to be performed – produced by decoder in cycle 3; B2 also holds info that will be needed for the write step (in next cycle) of I2
B3 holds results produced by exec unit and the destination info for I1

## Slide 44: Potential problems in pipelining
Mismatched stages: Different stages require different no. of cycles to finish e.g.: instruction fetch
  If a stage takes multiple cycles, it can be divided into more stages (one per clock cycle); as we said above, this results in more improvement of performance
  But what if previous instruction is a branch/jump?
  Especially problematic for conditional branches
    That is an instruction hazard: have to decide if branch/jump is taken or not before next instruction is fetched! (do you see why?)
    Generally, this is impossible, so have to stall the pipeline until the address of the next instruction is resolved (this is one of the reasons why we cannot achieve quite 1 instruction per clock cycle in a pipeline).
    Various solutions in both hardware and software (in compilers) have been tried

## Slide 45: Potential problems in pipelining-conditional branches
  But what if previous instruction is a branch/jump?
  Especially problematic for conditional branches
    That is an instruction hazard: have to decide if branch/jump is taken or not before next instruction is fetched! Why?
    If the conditional branch is taken, the next instruction to be fetched is at the address of the label encoded in the instruction;
    If the branch is NOT TAKEN, the next instruction to be fetched is at the address in the PC after being incremented.
    HOWEVER, the CPU does not determine if the branch will be taken or not till the end of the E stage (Execute stage) of the current instruction (that’s the stage in which the relevant flags are checked); by that time, the next instruction should already have been fetched!

## Slide 46: Conditional branch solution
The solution is to “stall” the pipeline till the E stage of the conditional branch instruction can be completed.
The pipeline will have to be stalled for two clock cycles (long enough for the E stage of the conditional branch instruction to complete).
“Stalling” the pipeline means that no work will be done for the following two instructions; the two following rows of the pipeline will be empty.
Of course, this results in a loss of performance; this is one of the reasons why pipelined processors cannot complete quite 1 instruction per clock cycle, and why 0.9 instructions per clock cycle is more usual.

## Slide 47: Potential problems in pipelining (contd)
Data hazards: if the data needed to execute an instruction is not yet available
  Maybe data needed has to be computed by previous instruction … can happen even in the case of register operands (how?)
  What if a result which is computed and written to a register by one instruction is needed for the E (Execute) stage of the following instruction?
  Again various solutions have been proposed for dealing with data hazards (example of a hardware solution: send the data directly to the buffer for another instruction which needs it, rather than writing it to a register or memory, and then reading it from there).

## Slide 48: Pipelining Conclusion
Even with the potential problems in pipelining (which can generally be addressed fairly successfully), pipelining still provides a really significant performance improvement!
For this reason, ALL modern CPUs are pipelined, usually with a pretty large number of stages (20 or more is typical today)!

## Slide 49: Multicore CPUs
Short story:
  For a long time, performance was improved by making clock faster; it roughly doubled every two years till about 2005
  HOWEVER: A faster clock increases power consumption, and therefore heat.
  Around 2005, heat was too great to cool CPU chips with ordinary methods (that is, without “exotic” cooling such as liquid cooling).
Therefore, architects looked for other ways to improve performance
CPUs with multiple cores were the common solution to increase performance; this allows the multiple cores to work on different programs at the same time (parallel processing)
We will say more about this in Part C of the course (on Operating Systems)

## Slide 50: Multicore CPUs cont.
Basically, multicore chips have multiple copies of the CPU parts we saw above, with one copy for each core (register set including PC, IR, flags, int registers, float registers, ALU, timing and control).
In order to take full advantage of the multiple cores, software has to use new techniques too (such as multi-threading).
If your CPU has 6 cores, for example, you can be running code for 6 different programs at once (or multiple threads of a multi-threaded program)!
We will look at multi-threading briefly in Part 3 of the course, on Operating Systems.
With multi-threading and multiprogramming, multicore CPUs can significantly improve performance.