## Slide 1: Assembly Language
Readings: 2.1-2.7, 2.9-2.10, 2.14
Green reference card
Assembly language
  Simple, regular instructions – building blocks of C, Java & other languages
  Typically one-to-one mapping to machine language
Our goal
Understand the basics of assembly language
Help figure out what the processor needs to be able to do
Not our goal to teach complete assembly/machine language programming
Floating point
Procedure calls
Stacks & local variables

## Slide 2: Aside: C/C++ Primer
struct coord { int x, y; }; /* Declares a type */
struct coord start; /* Object with two slots, x and y */
start.x = 1; /* For objects “.” accesses a slot */
struct coord *myLoc; /* “*” is a pointer to objects */
myLoc = &start; /* “&” returns thing’s location */
myLoc->y = 2; /* “->” is “*” plus “.” */
int scores[8]; /* 8 ints, from 0..7 */
scores[1]=5; /* Access locations in array */
int *index = scores; /* Points to scores[0] */
index++; /* Next scores location */
(*index)++; /* “*” works in arays as well */
index = &(scores[3]); /* Points to scores[3] */
*index = 9;
x
y
0
1
2
3
4
5
6
7

## Slide 3: ARM Assembly Language
The basic instructions have four components:
Operator name
Destination
1st operand
2nd operand
ADD <dst>, <src1>, <src2> // <dst> = <src1> + <src2>
SUB <dst>, <src1>, <src2> // <dst> = <src1> - <src2>
Simple format: easy to implement in hardware
More complex: A = B + C + D – E

## Slide 4: Operands & Storage
For speed, CPU has 32 general-purpose registers for storing most operands
For capacity, computer has large memory (multi-GB)
Load/store operation moves information between registers and main memory
All other operations work on registers
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output
GPRs

## Slide 5: Registers
32x 64-bit registers for operands
Register | Function | Comment
X0-X7 | Function arguments/Results | 
X8 | Result, if a pointer | 
X9-X15 | Volatile Temporaries | Not saved on call
X16-X17 | Linker scratch registers | Don’t use them
X18 | Platform register | Don’t use this
X19-X27 | Temporaries (saved across calls) | Saved on call
X28 | Stack Pointer | 
X29 | Frame Pointer | 
X30 | Return Address | 
X31 | Always 0 | No-op on write

## Slide 6: Basic Operations
(Note: just subset of all instructions)
Mathematic: ADD, SUB, MUL, SDIV ADD X0, X1, X2 // X0 = X1+X2
Immediate (second input a constant) ADDI X0, X1, #100 // X0 = X1+100
Logical: AND, ORR, EOR AND X0, X1, X2 // X0 = X1&X2
Immediate ANDI X0, X1, #7 // X0 = X1&b0111
Shift: left & right logical (LSL, LSR) LSL X0, X1, #4 // X0 = X1<<4
Example: Take bits 6-4 of X0 and make them bits 2-0 of X1, zeros otherwise:

## Slide 7: Memory Organization
Viewed as a large, single-dimension array, with an address.
A memory address is an index into the array
"Byte addressing" means that the index points to a byte of memory.
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 8: Memory Organization (cont.)
Bytes are nice, but most data items use larger units.
  Double-word = 64 bits = 8 bytes
  Word = 32 bits = 4 bytes
264 bytes with byte addresses from 0 to 264-1
261 double-words with byte addresses 0, 8, 16, ... 264-8
Double-words and words are aligned i.e., what are the least 3 significant bits of a double-word address?
0
8
16
24
64 bits of data
64 bits of data
64 bits of data
64 bits of data
Registers hold 64 bits of data

## Slide 9: Addressing Objects: Endian and Alignment
263..256
255..248
247..240
239..232
231..224
223..216
215..28
27..20
Doubleword:
Big Endian: address of most significant byte = doubleword address Motorola 68k, MIPS, IBM 360/370, Xilinx Microblaze, Sparc
Little Endian: address of least significant byte = doubleword address Intel x86, DEC Vax, Altera Nios II, Z80
ARM: can do either – this class assumes Little-Endian.
DWord 0
DWord 1
DWord 2
DWord 3
DWord 4
0
8
16
24
32
Big Endian
263..256
255..248
247..240
239..232
000
001
010
011
100
101
110
111
231..224
223..216
215..28
27..20
Little Endian
27..20
215..28
223..216
231..224
000
001
010
011
100
101
110
111
239..232
247..240
255..248
263..256

## Slide 10: Data Storage
Characters: 8 bits (byte)
Integers: 64 bits (D-word)
Array: Sequence of locations
Pointer: Address (64 bits)
// G = ASCII 71: 0x47 char a = ‘G’; int x = 258; // 0x102 char *b; int *y; b = new char[4]; y = new int[10];
0x1000
0x1001
0x1002
0x1003
0x1004
0x1005
0x1006
0x1007
0x1008
0x1009
0x100A
0x100B
0x100C
0x100E
0x100D
0x100F
0x1010
0x1011
0x1012
0x1013
0x1014
0x1015
0x1016
0x1017
0x1018
0x1019
0x101A
0x101B
0x101C
0x101E
0x101D
0x101F
0x1020
0x1021
0x1022
0x1023
0x1024
0x1025
0x1026
0x1027
0x1028
0x1029
0x102A
0x102B
0x102C
0x102E
0x102D
0x102F
(Note: real compilers place local variables (the “stack”) from beginng of memory, new’ed structures (the “heap”) from end. We ignore that here for simplicity)

## Slide 11: Loads & Stores
Loads & Stores move data between memory and registers
All operations on registers, but too small to hold all data
LDUR X0, [X1, #14] // X0 = Memory[X1+14]
STUR X2, [X3, #20] // Memory[X3+20] = X2
Note: LDURB & STURB load & store bytes
Store
Load
General
Purpose
Registers
X0:
X1:
X2:
X3:
130
723
4
Memory
24:
144:
66

## Slide 12: Addressing Example
The address of the start of a character array is stored in X0. Write assembly to load the following characters
X2 = Array[0]
X3 = Array[1]
X4 = Array[2]
X5 = Array[k] // Assume the value of k is in X1

## Slide 13: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
// Assume v in X0, k in X1
Store
Load
GPRs
X0:
X1:
X2:
X3:
X4:
928
10
Memory
0A12170D34BC2DE1
1000
1111111111111111
1008
0000000000000000
1016
FFFFFFFFFFFFFFFF
1032
0F0F0F0F0F0F0F0F
1024
FFFFFFFFFFFFFFFF
1040

## Slide 14: Execution Cycle Example
PC: Program Counter
IR: Instruction Register
Store
Load
General
Purpose
Registers
X0:
X1:
X2:
X3:
X4:
928
10
PC:
IR:
Memory
0000
0004
0008
0012
0016
0020
1000
1008
1016
1032
1024
1040
0A12170D34BC2DE1
1111111111111111
0000000000000000
FFFFFFFFFFFFFFFF
0F0F0F0F0F0F0F0F
FFFFFFFFFFFFFFFF
D3600C22
8B020002
F8400043
F8000044
F8408044
F8008043
Note:
Word addresses
Instructions are 32b
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 15: Flags/Condition Codes
Flag register holds information about result of recent math operation
Negative: was result a negative number?
Zero: was result 0?
Overflow: was result magnitude too big to fit into 64-bit register?
Carry: was the carry-out true?
Operations that set the flag register contents:
ADDS, ADDIS, ANDS, ANDIS, SUBS, SUBIS, some floating point.
Most commonly used are subtracts, so we have a synonym: CMP
  CMP X0, X1 same as SUBS X31, X0, X1
  CMPI X0, #15 same as SUBIS X31, X0, #15

## Slide 16: Control Flow
Unconditional Branch – GOTO different next instruction
B START // go to instruction labeled with “START” label
BR X30 // go to address in X30: PC = value of X30
Conditional Branches – GOTO different next instruction if condition is true
1 register: CBZ (==0), CBNZ (!= 0)
CBZ X0, FOO // if X0 == 0 GOTO FOO: PC = Address of instr w/FOO label
2 register: B.LT (<), B.LE(<=), B.GE (>=), B.GT(>), B.EQ(==), B.NE(!=)
first compare (CMP X0, X1, CMPI X0, #12), then b.cond instruction
CMP X0, X1 // compare X0 with X1 – same as SUBS X31, X0, X1
B.EQ FOO // if X0 == X1 GOTO FOO: PC = Address of instr w/FOO label
if (a == b)
a = a + 3;
else
b = b + 7;
c = a + b;
// X0 = a, X1 = b, X2 = c CMP X0, X1 // set flags B.NE ELSEIF // branch if a!=b ADDI X0, X0, #3 // a = a + 3 B DONE // avoid else ELSEIF: ADDI X1, X1, #7 // b = b + 7 DONE: ADD X2, X0, X1 // c = a + b

## Slide 17: Loop Example
Compute the sum of the values 0…N-1
int sum = 0; for (int I = 0; I != N; I++) { sum += I; }
// X0 = N, X1 = sum, X2 = I

## Slide 18: String toUpper
Convert a string to all upper case
char *index = string; while (*index != 0) { /* C strings end in 0 */ if (*index >= ‘a’ && *index <= ‘z’) *index = *index +(‘A’ - ‘a’); index++; }
// string is a pointer held at Memory[80]. // X0=index, ‘A’ = 65, ‘a’ = 97, ‘z’ = 122

## Slide 19: Machine Language vs. Assembly Language
Assembly Language
mnemonics for easy reading
labels instead of fixed addresses
Easier for programmers
Almost 1-to-1 with machine language
SWAP:
LSL X9, X1, #3
ADD X9, X0, X9 // Compute address of v[k]
LDUR X10, [X9, #0] // get v[k]
LDUR X11, [X9, #8] // get v[k+1]
STUR X11, [X9, #0] // save new value to v[k]
STUR X10, [X9, #8] // save new value to v[k+1]
BR X30 // return from subroutine
Machine language
Completely numeric representation
format CPU actually uses
11010011011 00000 000011 00001 01001
10001011000 01001 000000 00000 01001 11111000010 000000000 00 01001 01010
11111000010 000001000 00 01001 01011
11111000000 000000000 00 01001 01011
11111000000 000001000 00 01001 01010
11010110000 00000 000000 00000 11110

## Slide 20: Labels
Labels specify the address of the corresponding instruction
Programmer doesn’t have to count line numbers
Insertion of instructions doesn’t require changing entire code
Notes:
Branches are PC-relative
PC = PC + 4*(BranchOffset) BranchOffset positive -> branch downward. Negative -> branch upward.
// X0 = N, X1 = sum, X2 = I ADD X1, X31, X31 // sum = 0 ADD X2, X31, X31 // I = 0 TOP: CMP X2, X0 // Check I vs N B.GE END // end when !(I<N) ADD X1, X1, X2 // sum += I ADDI X2, X2, #1 // I++ B TOP // next iteration END:

## Slide 21: Labels Example
Compute the value of the labels in the code below.
  Branches: PC = PC + 4*(BranchOffset)
// Program starts at address 100 LDUR X0, [X31, #100] LOOP: LDURB X1, [X0, #0] CBZ X1, END CMPI X1, #97 B.LT NEXT CMPI X1, #122 B.GT NEXT SUBI X1, X1, #32 STURB X1, [X0, #0] NEXT: ADDI X0, X0, 1 B LOOP END:

## Slide 22: Instruction Types
Can group instructions by # of operands
3-register
2-register
1-register
0-register
ADD X0, X1, X2 ADDI X0, X1, #100 AND X0, X1, X2 ANDI X0, X1, #7 LSL X0, X1, #4 LSR X0, X1, #2 LDUR X0, [X1, #14] LDURB X0, [X1, #14] STUR X0, [X1, #14] STURB X0, [X1, #14] B START BR X30 CBZ X0, FOO B.EQ DEST

## Slide 23: Instruction Formats
All instructions encoded in 32 bits (operation + operands/immediates)
Branch (B-Type) Instr[31:21] = 0A0-0BF
Conditional Branch (CB-Type) Instr[31:21] = 2A0-2A7, 5A0-5AF
Register (R-Type) Instr[31:21] = 450-458, 4D6-558, 650-658, 69A-758
Immediate (I-Type) Instr[31:21] = 488-491, 588-591, 688-691, 788-791
Memory (D-Type) Instr[31:21] = 1C0-1C2, 7C0-7C2
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
BrAddr26
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
CondAddr19
Rd
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
Rm
Rn
Rd
SHAMT
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
ALU_Imm12
Rn
Rd
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
DT_Address9
Rn
Rd
00

## Slide 24: B-Type
Used for unconditional branches
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0 0 0 1 0 1
BrAddr26
0x05: B
B -3 // PC = PC + 4*-3
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00

## Slide 25: CB-Type
Used for conditional branches
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
CondAddr19
Rd
0x54: B.cond
0xB4: CBZ
0xB5: CBNZ
Condition Codes
0x00: EQ (==)
0x01: NE (!=)
0x0A: GE (>=)
0x0B: LT (<)
0x0C: GT (>)
0x0D: LE (<=)
Reg or Cond. Code
CBZ X12, -3 // if(X12==0) PC = PC + 4*-3
B.LT -5 // if (lessThan) PC = PC + 4*-5
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00

## Slide 26: R-Type
Used for 3 register ALU operations and shift
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
Rm
Rn
Rd
SHAMT
Shift amount
(0 for non-shift)
Op2
(0 for shift)
Op1
Dest
0x450: AND
0x458: ADD
0x4D6: SDIV, shamt=02
0x4D8: MUL, shamt=1F
0x550: ORR
0x558: ADDS
0x650: EOR
0x658: SUB
0x69A: LSR
0x69B: LSL
0x6B0: BR, rest all 0’s but Rd
0x750: ANDS
0x758: SUBS
ADD X3, X5, X6 // X3 = X5+X6
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
LSL X10, X4, #6 // X10 = X4<<6
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00

## Slide 27: I-Type
Used for 2 register & 1 constant ALU operations
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
ALU_Imm12
Rn
Rd
0x244: ADDI
0x248: ANDI
0x164: ADDIS
0x168: ORRI
0x344: SUBI
0x348: EORI
0x2C4: SUBIS
0x2C8: ANDIS
Constant - Op2
Op1
Dest
ADDI X8, X3, #35 // X8 = X3+35
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00

## Slide 28: D-Type
Used for memory accesses
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Opcode
DAddr9
Rn
Rd
00
Address Constant
Address Reg
Target Reg
0x1C0: STURB
0x1C2: LDURB
0x7C0: STUR
0x7C2: LDUR
LDUR X6, [X15, #12] // X6 = Memory[X15+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00

## Slide 29: Conversion example
Compute the sum of the values 0…N-1
ADD X1, X31, X31
ADD X2, X31, X31
B TEST TOP: ADD X1, X1, X2
ADDI X2, X2, #1 TEST: SUBS X31, X2, X0
B.LT TOP END:

## Slide 30: Assembly & Machine Language
Assembly
Machine Language