## Slide 1: Computer “Performance”
Readings: 1.6-1.8
BIPS (Billion Instructions Per Second) vs. GHz (Giga Cycles Per Second)
Throughput (jobs/seconds) vs. Latency (time to complete a job)
Measuring “best” in a computer
The PowerBook G4 outguns Pentium
III-based notebooks by up to 30 percent.*
* Based on Adobe Photoshop tests
comparing a 500MHz PowerBook G4 to
850MHz Pentium III-based portable computers
3.0 GHz
Hyper
Pipelined
Technology

## Slide 2: Performance Example: Homebuilders
Which is the “best” home builder?
Homeowner on a budget?
Rebuilding Haiti?
Moving to wilds of Alaska?
Which is the “speediest” builder?
Latency: how fast is one house built?
Throughput: how long will it take to build a large number of houses?
Builder | Time per House | Houses Per Month | House Options | Dollars Per House
Self-build | 24 months | 1/24 | Infinite | $200,000
Contractor | 3 months | 1 | 100 | $400,000
Prefab | 6 months | 1,000 | 1 | $250,000

## Slide 3: Computer Performance
Primary goal: execution time (time from program start to program completion)
To compare machines, we say “X is n times faster than Y”
Example: Machine Orange and Grape run a program
Orange takes 5 seconds, Grape takes 10 seconds
Orange is _____ times faster than Grape

## Slide 4: Execution Time
Elapsed Time
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes
CPU time
  doesn't count I/O or time spent running other programs
  can be broken up into system time, and user time
Example: Unix “time” command
linux15.ee.washington.edu> time javac CircuitViewer.java
3.370u 0.570s 0:12.44 31.6%
Our focus: user CPU time
  time spent executing the lines of code that are "in" our program

## Slide 5: CPU Time
Application example:
A program takes 10 seconds on computer Orange, with a 400MHz clock. Our design team is developing a machine Grape with a much higher clock rate, but it will require 1.2 times as many clock cycles. If we want to be able to run the program in 6 second, how fast must the clock rate be?
CPU execution time
for a program
CPU clock cycles
for a program
Clock period
=
*
CPU execution time
for a program
CPU clock cycles
for a program
1
Clock rate
=
*

## Slide 6: CPI
How do the # of instructions in a program relate to the execution time?
CPU clock cycles
for a program
Instructions
for a program
Average Clock
Cycles per Instruction
(CPI)
=
*
CPU execution time
for a program
Instructions
for a program
=
*
1
Clock rate
*
CPI

## Slide 7: CPI Example
Suppose we have two implementations of the same instruction set (ISA).
For some program
Machine A has a clock cycle time of 10 ns. and a CPI of 2.0 Machine B has a clock cycle time of 20 ns. and a CPI of 1.2
What machine is faster for this program, and by how much?

## Slide 8: Computing CPI
Different types of instructions can take very different amounts of cycles
Memory accesses, integer math, floating point, control flow
Instruction Type | Type Cycles | Type Frequency | Cycles * Freq
ALU | 1 | 50% | 
Load | 5 | 20% | 
Store | 3 | 10% | 
Branch | 2 | 20% | 
 |  | CPI: | 

## Slide 9: CPI & Processor Tradeoffs
How much faster would the machine be if:
A data cache reduced the average load time to 2 cycles?
Branch prediction shaved a cycle off the branch time?
Two ALU instructions could be executed at once?
Instruction Type | Type Cycles | Type Frequency
ALU | 1 | 50%
Load | 5 | 20%
Store | 3 | 10%
Branch | 2 | 20%

## Slide 10: Warning 1: Amdahl’s Law
The impact of a performance improvement is limited by what is NOT improved:
Example: Assume a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to speed up multiply to make the program run 4 times faster?
5 times faster?
Execution time
after improvement
Execution time
of unaffected
=
*
1
Amount of improvement
+
Execution time affected

## Slide 11: Warning 2: BIPs, GHz  Performance
Higher MHz (clock rate) doesn’t always mean better CPU
Orange computer: 1000 MHz, CPI: 2.5, 1 billion instruction program
Grape computer: 500MHz, CPI: 1.1, 1 billion instruction program
Higher MIPs (million instructions per second) doesn’t always mean better CPU
1 GHz machine, with two different compilers
Compiler A on program X: 10 Billion ALU, 1 Billion Load
Compiler B on program X: 5 Billion ALU, 1Billion Load
Execution Time: A ____ B ____
BIPS: A ____ B ____
Instruction Type | Type Cycles
ALU | 1
Load | 5
Store | 3
Branch | 2

## Slide 12: Processor Performance Summary
Machine performance:
Better performance:
_____ number of instructions to implement computations
_____ CPI
_____ Clock rate
Improving performance must balance each constraint
Example: 1980’s RISC vs. CISC
CPU execution time
for a program
Instructions
for a program
=
*
1
Clock rate
*
CPI