## Slide 1: Memory Hierarchy: Caches, Virtual Memory
Readings: 5.1-5.4, 5.8
Big memories are slow
Fast memories are small
Need to get fast, big memories
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output

## Slide 2: Random Access Memory
Dynamic Random Access Memory (DRAM)
  High density, low power, cheap, but slow
  Dynamic since data must be “refreshed” regularly
  Random Access since arbitrary memory locations can be read
Static Random Access Memory
  Low density, high power, expensive
  Static since data held as long as power is on
  Fast access time, often 2 to 10 times faster than DRAM
Technology | Access Time | Cost/Capacity
SRAM | 1-7 cycles | 10,000x
DRAM | 100 cycles | 200x
Disk | 10K – 10M cycles | 1x

## Slide 3: The Problem
Cost vs. Performance
Fast memory is expensive
Slow memory can significantly affect performance
Design Philosophy
Use a hybrid approach that uses aspects of both
Keep frequently used things in a small amount of fast/expensive memory
“Cache”
Place everything else in slower/inexpensive memory (even disk)
Make the common case fast

## Slide 4: Locality
Programs access a relatively small portion of the address space at a time
Types of Locality
  Temporal Locality – If an item has been accessed recently, it will tend to be accessed again soon
  Spatial Locality – If an item has been accessed recently, nearby items will tend to be accessed soon
Locality guides caching
char *index = string; while (*index != 0) { /* C strings end in 0 */ if (*index >= ‘a’ && *index <= ‘z’) *index = *index +(‘A’ - ‘a’); index++; }

## Slide 5: The Solution
By taking advantage of the principle of locality:
  Provide as much memory as is available in the cheapest technology.
  Provide access at the speed offered by the fastest technology.
Control
Datapath
Secondary
Storage
(Flash)
Processor
Registers
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
On-Chip
Cache
Name Register Cache Main Memory Disk Memory
Speed 1 cycle 1-7 cycles 100 cycles 10,000 cycles Capacity 1x (norm.) 64-4Kx 4Mx 1Gx

## Slide 6: Cache Terminology
Block – Minimum unit of information transfer between levels of the hierarchy
  Block addressing varies by technology at each level
  Blocks are moved one level at a time
Upper vs. lower level – “upper” is closer to CPU, “lower” is futher away
Hit – Data appears in a block in that level
Hit rate – percent of accesses hitting in that level
Hit time – Time to access this level
Hit time = Access time + Time to determine hit/miss
Miss – Data does not appear in that level and must be fetched from lower level
Miss rate – percent of misses at that level = (1 – hit rate)
Miss penalty – Overhead in getting data from a lower level
Miss penalty = Lower level access time + Replacement time + Time to deliver to processor
Miss penalty is usually MUCH larger than the hit time

## Slide 7: Cache Access Time
Average access time
  Access time = (hit time) + (miss penalty)x(miss rate)
  Want high hit rate & low hit time, since miss penalty is large
Average Memory Access Time (AMAT)
Apply average access time to entire hierarchy.

## Slide 8: Cache Access Time Example
Note: Numbers are local hit rates – the ratio of access that go to that cache that hit (remember, higher levels filter accesses to lower levels)
Level | Hit Time | Hit Rate | Access Time
L1 | 1 cycle | 95% | 
L2 | 10 cycles | 90% | 
Main Memory | 50 cycles | 99% | 
Disk | 50,000 cycles | 100% | 

## Slide 9: Handling A Cache Miss
Processor expects a cache hit (1 cycle), so no effect on hit.
Instruction Miss
1. Send the original PC to the memory
2. Instruct memory to perform a read and wait (no write enables)
3. Write the result to the appropriate cache line
4. Restart the instruction
Data Miss
1. Stall the pipeline (freeze following instructions)
2. Instruct memory to perform a read and wait
3. Return the result from memory and allow the pipeline to continue

## Slide 10: Exploiting Locality
Spatial locality
  Move blocks consisting of multiple contiguous words to upper level
Temporal locality
  Keep more recently accessed items closer to the processor
  When we must evict items to make room for new ones, attempt to keep more recently accessed items

## Slide 11: Cache Arrangement
How should the data in the cache be organized?
Caches are smaller than the full memory, so multiple addresses must map to the same cache “line”
Direct Mapped – Memory addresses map to particular location in that cache
Fully Associative – Data can be placed anywhere in the cache
N-way Set Associative – Data can be placed in a limited number of places in the cache depending upon the memory address

## Slide 12: Direct Mapped Cache
4 byte direct mapped cache with 1 byte blocks
Optimize for spatial locality (close blocks likely to be accessed soon)
0
1
2
3
4
5
6
7
8
9
A
B
C
E
D
F
0
1
2
3
Memory Address
Cache Address

## Slide 13: Finding A Block
Each location in the cache can contain a number of different memory locations
Cache 0 could hold 0, 4, 8, 12, …
We add a tag to each cache entry to identify which address it currently contains
What must we store?

## Slide 14: Cache Tag & Index
Assume 29 byte direct mapped cache with 1 byte blocks
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 0 0 1
Cache Tag = 57
0 0 0 0 0 0 0 1 1
Cache Index=03
0
1
2
3
4
5
6
7
29-1
…
…
…
…
Valid Bit
Tag
Data

## Slide 15: Cache Access Example
Assume 4 byte cache
Access pattern:
00001
00110
00001
11010
00110
0
1
2
3
Valid Bit
Tag
Data

## Slide 16: Cache Size Example
How many total bits are requires for a direct-mapped cache with 64 KB of data and 1-byte blocks, assuming a 32-bit address?
Index bits:
Bits/block:
Data:
Valid:
Tag:
Total size:

## Slide 17: Cache Block Overhead
Previous discussion assumed direct mapped cache 1 byte blocks
  Uses temporal locality by holding on to previously used values
  Does not take advantage of spatial locality
  Significant area overhead for tag memory
Take advantage of spatial locality & amortize tag memory via larger block size
0
1
2
3
4
5
6
7
2n-1
…
…
…
…
Valid Bit
Tag
Data
…
…
…

## Slide 18: Cache Blocks
Assume 210 line direct mapped cache with 29 byte blocks
0
1
2
3
4
5
6
7
210-1
…
…
…
…
Valid Bit
Tag
Data
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0 0 0 0 0 0 0 1 1 1 0 1 0
Cache Tag = 58
0 0 0 0 0 0 0 0 1
Byte Select = 1
0 0 0 0 0 0 0 1 0 0
Cache Index = 4
…
…
…
0
1
29-1

## Slide 19: Cache Block Example
Given a cache with 64 blocks and a block size of 16 bytes, what are the byte select, cache index, and tag for byte address 120010?
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00

## Slide 20: Block Size Tradeoff
In general, larger block size take advantage of spatial locality BUT:
  Larger block size means larger miss penalty:
    Takes longer time to fill up the block
  If block size is too big relative to cache size, miss rate will go up
    Too few cache blocks
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Block Size

## Slide 21: Direct Mapped Cache Problems
What if regularly used items happen to map to the same cache line?
Ex. &(sum) = 0, &(I) = 64, cache is 64 bytes
Thrashing – Continually loading into cache but evicting it before reuse
int sum = 0;
… for (int I=0; I!=N; I++) { sum += I; }
0
1
2
3
4
5
6
7
63
…
…
…
…
Valid Bit
Tag
Data

## Slide 22: Cache Miss Types
Several different types of misses (categorized based on problem/solution)
  3 C’s of cache design
Compulsory/Coldstart
  First access to a block – basically unavoidable (though bigger blocks help)
  For long-running programs this is a small fraction of misses
Capacity
  The block needed was in the cache, but unloaded because too many other accesses intervened.
  Solution is to increase cache size (but bigger is slower, more expensive)
Conflict
  The block needed was in the cache, and there was enough room to hold it and all intervening accesses, but blocks mapped to the same location knocked it out.
Solutions
Cache size
Associativity
Invalidation
I/O or other processes invalidate the cache entry

## Slide 23: Categorizing misses amongst the 3 C’s
Have you touched
this block before?
Is # of unique blocks touched since last touch ≥ cache size?
Cache Miss
Coldstart
(Inevitable)
Capacity
(Cache too small)
Conflict
(Cache too dumb)
Yes
No
Yes
No

## Slide 24: Fully Associative Cache
No cache index – blocks can be in any cache line
0
1
2
3
4
5
6
7
2n-1
…
…
…
…
Valid Bit
Tag
Data
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 0 0 1
Cache Tag = 57
0 0 0 0 0 0 0 0 1
Byte Select=01
…
…
…
0
1
2m-1
= =?
= =?
= =?
= =?
= =?
= =?
= =?
= =?
= =?

## Slide 25: Fully Associative vs. Direct Mapped

## Slide 26: N-way Set Associative
N lines are assigned to each cache index
~ N direct mapped caches working in parallel
Direct mapped = 1-way set associative
Fully Associative = 2N-way set associative (where 2N is # of cache lines)

## Slide 27: 2-Way Set Associative Cache
Cache index selects a “set”, two tags compared in parallel
= =?
…
Valid
…
Tag
Block
…
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Cache Tag = 57
Byte Select=01
Cache Index = 04
…
Valid
…
Tag
Block
…
= =?
Addr Cache Tag
Addr Cache Tag
Hit
Cache Block

## Slide 28: N-way vs. Other Caches

## Slide 29: Cache Miss Comparison
Fill in the blanks: Zero, Low, Medium, High, Same for all
 | Direct Mapped | N-Way Set Associative | Fully Associative
Cache Capacity: Small, Medium, Big? |  |  | 
Compulsory/Coldstart Miss: |  |  | 
Capacity Miss |  |  | 
Conflict Miss |  |  | 
Invalidation Miss | Same | Same | Same

## Slide 30: Complex Cache Miss Example
8-word cache, 2-word blocks. Determine types of misses (CAP, COLD, CONF).
Byte Addr | Block Addr | Direct Mapped | 2-Way Assoc | Fully Assoc
0 |  |  |  | 
4 |  |  |  | 
8 |  |  |  | 
24 |  |  |  | 
56 |  |  |  | 
8 |  |  |  | 
24 |  |  |  | 
16 |  |  |  | 
0 |  |  |  | 
Total: |  |  |  | 

## Slide 31: Writing & Caches
Direct-mapped cache with 16-byte blocks, initially empty
Main Memory:
Cache Line:
STUR X0, [X31, #0]

## Slide 32: Writing & Caches (cont.)

## Slide 33: Replacement Methods
If we need to load a new cache line, where does it go?
Direct-mapped
Set Associative
Fully Associative

## Slide 34: Replacement Strategies
When needed, pick a location
Approach #1: Random
  Just arbitrarily pick from possible locations
Approach #2: Least Recently Used (LRU)
  Use temporal locality
  Must track somehow – extra cache bits to indicate how recently used
In practice, Random typically only 12% worse than LRU

## Slide 35: Split Caches
Instruction vs. Data accesses
  How do the two compare in usage?
  How many accesses/cycle do we need for our pipelined CPU?
Typically split the caches into separate instruction, data caches
Higher bandwidth
Optimize to usage
Slightly higher miss rate because each cache is smaller.

## Slide 36: Multi-level Caches
Instead of just having an on-chip (L1) cache, an off-chip (L2) cache is helpful
Ex. Base machine with CPI = 1.0 if all references hit the L1, 2 GHz
Main memory access delay of 50ns. L1 miss rate of 5%
How much faster would the machine be if we added a L2 with a miss rate of 10%, and an access time of 20ns.

## Slide 37: Cache Summary

## Slide 38: Virtual Memory
Disk more cost effective than even DRAM
Use Disk as memory?
Virtual Memory: View disk as the lowest level in the memory hierarchy
“Page” memory to disk when information won’t fit in main memory
Technology | Access Time | Cost/Capacity
SRAM | 1-7 cycles | 10,000x
DRAM | 100 cycles | 200x
Disk | 10K – 10M cycles | 1x

## Slide 39: Virtual Addresses
Thought experiment: What happens when you run two programs at once?
  How do they share the address space?
Solution: Virtual addresses
  Each address the processor generates is a Virtual Address
  Virtual Addresses are mapped to Physical Addresses
  Virtual address may correspond to address in memory, or to disk
Other important terminology
  Page – the block for main memory, moved as a group to/from disk
  Page fault – “miss” on main memory. Handled as a processor exception
  Memory mapping/address translation – conversion process from virtual to physical addresses

## Slide 40: Virtual to Physical Addresses
Virtual Addresses
Physical Addresses
Disk Addresses
Address
Translation
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Virtual Page Number
Page Offset
Virtual Address:
Physical Page Number
Page Offset
Physical Address:
Translation

## Slide 41: Virtual Memory Summary
Main Memory is a cache
  Large cache lines/page size – spatial locality
  Huge page fault/cache miss penalty – fully associative, software managed
  Translation complex – cache the misses themselves
Thrashing