## Slide 1
CSE 3430
Y86 Assembly Language – Part B

## Slide 2: Y86 Instruction Types
Data movement Instructions
Arithmetic and Logical (ALU) Instructions
Control-flow Instructions (used to implement if/else, loops, function calls/return in high-level languages)
AFTER WE UNDERSTAND THESE INSTRUCTIONS, we still need a stack to call functions, in order to (a) pass parameters to them, and (b) save the return address back to the calling function.

## Slide 3
Y86 Assembly Language –
Data Movement Instructions

## Slide 4
4
Y86-64 Instructions
Operations on 8-byte integers (no floating point operations!)  “word” (NOTE: it is considered a “quad” word (64 bits) for historical reasons, because a word in the original Intel architecture was16 bits!)
Format of instructions
  - 1–10 bytes of information read from memory (variable instruction length – CISC feature)
    - Can determine the type of instruction from first byte
    - Can determine instruction length from first byte
Registers
  - rA or rB represent one of the 15 registers (0-14)
  - 0xF denotes “no register” (some instructions only use 1 register)
  - No “partial” register options (must be a full 8-bit byte – actually, divided into two half-bytes - to encode which register(s) used, or no register)
Notes: No floating point registers or instructions
4

## Slide 5: Y86-64 Move Instructions
Split into four different instructions, with “prefix”
Explicitly indicates source (1st char of instruction name) and destination (2nd char of instruction name)
  Immediate (i) – always a CONSTANT operand (data or address)
  Register (r)
  Memory (m) – base + displacement format
Either Source, or Destination or both must be a register (immediate to memory, or memory to memory not possible)
rrmovq rA, rB
2
0
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 6: Notes on Y86 Instruction Encoding
The first byte (two hex digits) is an opcode; this identifies the type of instruction for the CPU.
The second byte identifies one or two registers – each of the 15 registers has a number, 0 to f; the CPU uses these numbers, and not names such as rax, rbx, etc.
For data movement instructions which use data in memory, the last 8 bytes are used for a constant (stored in the instruction) or for a displacement (added to an address stored in a register).

## Slide 7: Source and Destination
For Y86-64 instructions that have two operands:
  The first operand is always the source operand, and the second operand is the destination operand.
  The source operand is always read by the CPU, but never written (it never ever changes when the instruction is executed).
  The destination operand is always written (so the old value is overwritten and lost); it is ALSO read for ALU instructions, but not for data movement instructions.

## Slide 8: One operand instructions
There are a few instructions that have only a single operand.
In such instructions, the operand can be a source or a destination; we have to learn which it is for each type of instruction.
There are a small number of these, so it is not too difficult to learn them (we will cover them later).

## Slide 9: Type of operands in Y86-64
Y86 has three types of operands:
  Immediate: This is always an 64-bit (8-byte) constant, and is stored in the instruction (as part of the bit string which encodes the instruction).
  Register: This is an 8-byte value in one of the 15 registers in Y86-64 (rax, rbx, …., r14).
  Memory: This is an 8-byte value at some address in main memory.

## Slide 10: Move Operations
irmovq is used to place 8 byte immediate (constant) values (addresses of labels or numeric literal constants) into a register
rrmovq copies a value between registers
rmmovq stores a word in memory
mrmovq loads a word from memory
rmmovq and mrmovq are THE ONLY INSTRUCTIONS THAT ACCESS MEMORY – Y86 is a load/store architecture – RISC feature)
Direct transfers from one memory location to another are not allowed (must move through a register)
Transfer of immediate data to memory is not allowed

## Slide 11: Important note for 2 operand instructions!
When data is moved or an ALU operation on data is done, the data in the register or location in memory which is read (the first operand in the instruction – called a source operand) IS NOT CHANGED!
Only the data in the second operand (called a destination operand – the one which is written) is changed.
As mentioned before, the second (destination) operand is also read for ALU instructions, but not for data movement instructions.

## Slide 12
Assembly Syntax
AT&T (Used in Unix/Linux environments)  What Y86 assembler uses
  - Immediate (constant) values preceded by $
  - Registers are prefixed with %
  - Effective address DISP(BASE)
  *The BASE address must be in a register
  *The DISP is a displacement added to the base address in the register, and it is optional; if present, it can be positive, zero, or negative.
  - Moves and ALU operations are source, destination:
    irmovq $5, %rax
There is also an Intel syntax (pretty different and generally less clear), but we will not study it.

## Slide 13
Simple Addressing Modes
13
We can treat Registers as an array of size 15 called Reg: Register R is Reg[R] [15 is a strange number! The number of registers is a power of 2 in real CPUs]
Memory is treated as an array called Mem, indexed from 0 to size of memory – 1.
Normal Addressing = (R) = Mem[Reg[R]]
  - Register Reg[R] contents specify memory address
  - Example: mrmovq (%rcx),%rax
Displacement Addressing = D(R) = Mem[Reg[R]+D]
  - Register R contents specify start of memory region
  - Constant displacement D specifies offset in bytes
  Example: mrmovq 8(%rbx),%rdx
  If rbx has 1000, this would read from address 1008 and write value read to register rdx.

## Slide 14
2) Arithmetic and Logical Instructions

## Slide 15
15
Supported ALU Operations
Arithmetic instructions
  - addq rA, rB R[rB] ← R[rB] + R[rA]
  - subq rA, rB R[rB] ← R[rB] − R[rA]
  - andq rA, rB R[rB] ← R[rB] & R[rA]
  - xorq rA, rB R[rB] ← R[rB] ^ R[rA]
# y86prog2.ys
.pos 0x0
irmovq $1, %rax
irmovq $0, %rbx
irmovq $1, %rcx
addq %rax, %rax
andq %rbx, %rbx
subq %rax, %rcx
irmovq $0x7fffffffffffffff, %rdx
addq %rdx, %rdx
halt
% yas y86prog2.ys
% yis y86prog2.yo
Stopped in 9 steps at PC = 0x2a.
Status 'HLT‘, CC Z=0 S=1 O=1
Changes to registers:
%rax: 0x0000000000000000 0x0000000000000002
%rcx: 0x0000000000000000 0xffffffffffffffff
%rdx: 0x0000000000000000 0xfffffffffffffffe
Changes to memory:
Notes: Notice & ^ are bit operations
Watch out for subl command – correct order very important!
What are the CC bits for each instruction for the example code?
15

## Slide 16: Flag changes
Consider how the flags change for each of the instructions in the program on the prior slide:
  ZF, SF, OF
  Let’s trace the execution, and see how the flags change.
Remember that ONLY ALU instructions write/change the flags (also called condition codes)
  Data movement and control flow instructions (covered below) NEVER EVER change the flags!

## Slide 17: Flags/Condition codes – for code on slide 16 above
irmovq $1, %rax #rax has 1
irmovq $0, %rbx #rbx has 0
irmovq $1, %rcx #rcx has 1
addq %rax, %rax # z = 0, s = 0, o = 0
andq %rbx, %rbx # z = 1, s = 0, o = 0
subq %rax, %rcx # z = 0, s = 1, o = 0
irmovq $0x7fffffffffffffff, %rdx #0x7 is 0111 binary, and 0xf is 1111 binary
%rdx has msb of 0, followed by 63 1’s;
#this is largest positive int in 64 bits
addq %rdx, %rdx # z = 0, s = 1, 0 = 1 ; overflow here!
halt

## Slide 18
3) Control Flow Instructions

## Slide 19: Control Flow Instructions
Y86 has, as almost all processors do, the control flow instructions listed below
Jumps (A DIFFERENT TERM for branches):
  Unconditional: jmp (jumps regardless of flag settings)
  Conditional: je, jne, jl, jle, jg, jge (jump depends on settings of relevant flags - see below)
call or callq: call instruction for functions/subroutines
ret: return from function/subroutine
halt: stops the simulated processor

## Slide 20: Labels
All assembly language jump instructions use a label
Any label before code (a function or loop, for example) or data must be followed by a colon (the following colon is how the assembler identifies the label as a label).
A label is a string, which must start with an alphabetic character, followed by zero or more alphanumeric characters, for example:
  loop
  Loop1
  sum
  findMin
When the assembler assembles the program, it will replace each label by the corresponding address (the address of the label). Therefore, there are no labels in machine code, but only addresses.

## Slide 21
21
Jump instruction types
Unconditional jump
  - jmp Dest PC ← Dest
Conditional jumps
  - jle Dest PC ← Dest iff last result ≤ 0
    SF=1 OR ZF=1
  - jl Dest PC ← Dest iff last result < 0
    SF=1 (AND ZF=0)
  - je Dest PC ← Dest iff last result = 0
    ZF=1
  - jne Dest PC ← Dest iff last result ≠ 0
    ZF=0
  - jge Dest PC ← Dest iff last result ≥ 0
    SF=0 OR ZF=1
  - jg Dest PC ← Dest iff last result > 0
    SF=0 AND ZF=0
If the last result is not what is specified, then the jump is not taken; in that case, the next sequential instruction is executed i.e.,
PC = PC + jump instruction size
What about checking OF?
Notes: Notice and/or options for flags as well as some only check one flag and others check two flags
21

## Slide 22
22
Y86 example program w/ loop
# y86loop.ys
.pos 0x0
irmovq $0,%rax # sum = 0
irmovq $1,%rcx # num = 1
Loop:
addq %rcx,%rax # sum += num
irmovq $1,%rdx # tmp = 1
addq %rdx,%rcx # num++
irmovq $1000,%rdx # lim = 1000
subq %rcx,%rdx # if lim - num >= 0
jge Loop # loop again
halt
Which instructions set the CC (condition code) or flag bits?
What are the flags set to for each instruction?
CONVERT TO C
sum=0;
num = 1;
do {
sum += num;
num++;
}
while (1000 – num >= 0)
Notes: Technically, the bits are set to ZF=1, SF=0 and OF=0 when the program starts
22

## Slide 23
23
Y86 example program w/ loop
# y86loop.ys
.pos 0x0
irmovq $0,%rax # sum = 0
irmovq $1,%rcx # num = 1
Loop:
addq %rcx,%rax # sum += num
irmovq $1,%rdx # tmp = 1
addq %rdx,%rcx # num++
irmovq $1000,%rdx # lim = 1000
subq %rcx,%rdx # if lim - num >= 0
jge Loop # loop again
halt
Why don’t we just do addq $1, %rcx??
CAN’T! NOT ALLOWED, because both operands of an ALU operation must be in registers (no constant or memory operands in Y86 for ALU instructions)
CONVERT TO C
sum=0;
num = 1;
do {
sum += num;
num++;
}
while (1000 – num >= 0)
Notes: 23

## Slide 24
24
Result of y86loop.ys
% yis y86loop.yo
Stopped in 6003 steps at PC = 0x37.
Status 'HLT', CC Z=0 S=1 O=0
Changes to registers:
%rax: 0x00000000 0x000000000007a314
%rcx: 0x00000000 0x00000000000003e9
%rdx: 0x00000000 0xffffffffffffffff
EXPLANATION:
Sum of 1 to 1000 = 500500 = 0x7a314 = %rax
0x3e9 = 1001 = %rcx
CC sign bit = 1 because 1000 – 1001 = -1 =
0xffffffffffffffff = %rdx

## Slide 25: call and ret instructions
Similarly to jump instructions, the call instruction uses a label (shown as Dest below):
call Dest
  This instruction will (1) push the return address (the address of next instruction after the call instruction) on the stack, and (2) write the address of the Dest label to the PC, so the Dest function’s code will execute next.
ret
  This is the ret instruction, which will (1) pop the return address from the stack, and (2) write it to the PC

## Slide 26: The stack – needed to call functions
Because the call instruction pushes a return address onto the stack, and because the ret instruction pops a return address off of the stack, we also need a stack if we wish to call functions.
In Y86-64, if we want to use a stack, we have to set it up explicitly (there is no Operating System, or OS, which provides a stack to us for our use).
Since you will not be asked to write Y86-64 programs, you do not need to know how to write stack set up code, but we cover it so you understand it (and you should understand it).

## Slide 27: Note about subroutine terms
Remember that function, procedure and method are high-level language terms for subroutines (the assembly/machine language term).
For the processor, these are all the same thing; that is, they are all subroutines.
So, in machine language, there are only subroutines, but we can refer to them as functions, and we usually do.

## Slide 28: More on the stack
The program stack is actually divided conceptually into frames.
Each procedure or function (main and any functions called from main or from another function) has its own part of the stack to use, which is called its frame.
The frame goes from the stack address pointed to by %rbp in that function (this is called the base pointer or frame pointer; it points to the bottom of the function’s stack frame), to %rsp, which points to the top of the stack while the procedure is running.
This implies that the address pointed to by %rbp is different in different functions: %rbp must be set when the function is entered.

## Slide 29: Stack instructions
There are two other stack instructions which we did not see before, but if you are familiar with the LIFO (Last-In-First-Out) nature of a stack, they are easy:
pushq rA #This reads the value in register rA, and
#pushes it onto the top of the stack (it
#decrements %rsp by 8 bytes before writing
#the value to (%rsp).
popq rB #This reads the value which is at the top of
#the stack, and writes a copy of it to register
#rB; %rsp is also incremented by 8 bytes after (%rsp) is
#read.

## Slide 30: Preparing the stack for the function to run
For the function to be able to use the stack, we have to set the frame pointer, %rbp, to the bottom of its frame (which is the top of the stack before the function begins execution).
Before we can do this, though, we must save the frame pointer of the caller, or it will be lost after return!
After saving the frame pointer of the caller, we will make the function’s frame pointer point to the saved caller’s frame pointer; therefore, in any function (except main), %rbp should point to the saved caller’s frame pointer.
The following slide shows the instructions we put at the beginning of the function to do these things.

## Slide 31: Setting the procedure’s stack frame
pushq %rbp #Save the caller’s base pointer
rrmovq %rsp, %rbp #Set the procedure’s base pointer
Notice that, after the second instruction above, the procedure’s stack frame only has the caller’s saved frame pointer; rbp now points to the saved caller’s frame pointer.

## Slide 32: Setting up function’s stack frame
To set the function’s stack frame, these instructions must be executed:
pushq %rbp #Save caller’s frame pointer
rrmovq %rsp, %rbp #Set function’s frame pointer
Notice that, after the second instruction above, the function’s stack frame only has the caller’s saved frame pointer; rbp now points to the saved caller’s frame pointer.

## Slide 33: How to set up the stack
In typical systems, the stack starts at a very high address, and as data is pushed onto the stack, it grows downward in memory (to lower numbered addresses).
Therefore, we should put the bottom of our stack at a high address (so we have space for it to grow down enough for the stack frames of our functions).
We will use the address 0x1000 (Hex 1000 – this is 1 X 163, or 212, which is decimal 4096); this is actually not a very high address, but for the relatively simple programs we use, it will be high enough to have enough space for our stack frames.

## Slide 34: Reminder: Y86 Stack
Stack top address always held in register %rsp
Stack grows towards lower addresses:
This means the stack grows downward
in memory.
%rsp
•
•
•
Increasing
Addresses
Stack “Bottom”
Stack “Top”

## Slide 35: Code to set up the stack
We need a .pos directive, a .align directive, and a label:
.pos 0x1000
.align 8
stack:
Code at the beginning of main:
main:
  irmovq stack, %rbp #rbp has address of bottom
  # of stack frame
  rrmovq %rbp, %rsp #rsp is stack pointer – now has #address of bottom of stack

## Slide 36: Putting arrays in memory
We can also put data in memory which we want our program to be able to do work on.
Suppose we want an array of signed integers with 6 elements, and we wish to call it “array” (How creative!!).
See the next slide

## Slide 37: Placing array in memory
#Note: Comments are preceded by a #
.pos 0x900 #well below the bottom of our stack)
.align 8
array: #Label for array data
.quad 2
.quad 3
.quad 9
.quad 5
.quad 4
.quad 7
size: #Label for size of array
.quad 6

## Slide 38: A place for output
We should also make a place to “write,” or move, output for the program, so that we can see what the program did:
.align 8
.pos 0x800
output: #output label

## Slide 39: Passing parameters to functions
In most architectures, the stack is also used to pass parameters to functions.
  The pushq instruction is used in the calling function's code to place parameters on the stack.
  To read/get parameters from the stack, the calling function DOES NOT USE popq (because this would require popping other items off of the stack that we don't want to remove, such as the return address back to the caller!)
  INSTEAD, mrmovq is used to read parameters from the stack and put them in registers for the callee function to use in executing its code. (See example later.)

## Slide 40: Convention for parameter passing
Parameters are passed on the stack, and are placed on the stack before the function to which they are passed is called.
If you think about it, there must be some order specified for the parameters, and this is set by a convention (all functions which are going to pass or get parameters must follow this convention).
The convention says that the parameters are pushed onto the stack from the last one listed to the first one listed in the function’s parameters.

## Slide 41: Example program
Next,we consider a very simple program with two functions, main and sum.
The sum function is passed two parameters, as shown below:
quad sum (array, size);
Since the size parameter is listed last, it will be pushed onto the stack first. Since the array parameter is listed first, it will be pushed onto the stack last before calling the function (which will push the return address onto the stack).

## Slide 42: Program code
See the file y86sum.pdf on Carmen for the program code.
We will go over this code in the next class.