## Slide 1: Dynamic Branch Prediction
Readings: 4.8
Branches introduce control hazards
Determine the right next instruction in time for instruction fetch
Previous solutions:
Stall
Statically predict not taken
Branch Delay slot
Better:
Branch-prediction buffers (caches)

## Slide 2: Problems With Static Branch Predictors
Are all conditional branches created equal?

## Slide 3: Branch Prediction Buffer
Direct-mapped cache w/1-bit history
  Predict taken/not taken by previous execution
  If incorrect prediction, annul instructions incorrectly started
Tags?
Valid bits?

## Slide 4: Thought Experiment
Consider the following code segment:
while (1) {
<code 1>
for(int i=0; i<9; i++) {
<code 2>
}
<code 3>
}
1-bit prediction accuracy?
ADDI C, X31, #9 // Const. 9
WHILE_TOP:
<code 1>
ADD i, X31, X31 // Init i
B FOR_TEST
FOR_TOP:
<code 2>
ADDI i, i, #1 // i++
FOR_TEST:
CMP i, C // i < 9?
B.LT FOR_TOP
<code 3>
B WHILE_TOP // Endwhile

## Slide 5: 2-bit Predictor

## Slide 6: 2-bit Predictor (cont.)
while (1) {
if (normal_condition) {
<code1>
}
for(int i=0; i<9; i++) {
if (exception) {
return (FALSE);
}
<code 2>
}
if (random 50/50 chance) {
<code 3>
}
}
2
# of predictors
Branch Predictor

## Slide 7: Instruction-Level Parallelism & Advanced Architectures
Readings: 4.10
Key to pipelining was dealing with hazards
Advanced processors require significant hazard avoidance/flexibility
ILP = Instruction-Level Parallelism

## Slide 8: Why ILP
Advanced processors optimize two factors:
Reduce clock period by heavy pipelining
Greater pipelining means more hazards, delay slots
Reduce CPI
What if we want a CPI < 1.0?

## Slide 9: ILP Example
Source code:
ADDI X0, X0, #15
SUB X2, X1, X0
EORI X3, X0, #15
ORR X4, X3, X0
Constraint graph:

## Slide 10: Complex ILP Example
Note: Assume no delay slots.
1: LDUR X0, [X3, #0]
2: ADD X1, X0, X2
3: SUB X2, X3, X4
4: ANDI X2, X5, #57
5: ORR X7, X5, X1
6: STUR X5, [X9, #0]
7: CBZ X7, LOOP
8: EOR X6, X8, X6

## Slide 11: Types of Hazards
Data Hazards (multiple uses of the same location)
RAW – Read after write
WAW – Write after write
WAR – Write after read
RAR – Read after read
Memory
Control Hazards
Branches

## Slide 12: Hazard Minimization
Hardware and software techniques for improving performance
  Loop unrolling
  Register Renaming
  Predicated Instructions
Responsibility
Hardware
Software (Compiler)

## Slide 13: Loop-Level Parallelism
LLPex(char *src) {
char *end = src + 1000;
while(src<end) {
*src = (*src)+3; src++;} }

## Slide 14: Loop Unrolling
Better loop structure?

## Slide 15: Compiler Register Renaming
Compiler reduces hazards by removing name dependences

## Slide 16: Hardware Register Renaming
CPU dynamically associates each register read with the most recent instruction issue that writes that register.
0: ADDI X0, X0, #8
1: LDUR X1, [X0, #0]
2: STUR X1, [X0, #100]
3: ADDI X0, X0, #8
4: LDUR X1, [X0, #0]
5: STUR X1, [X0, #100]
6: ADDI X0, X0, #8
7: LDUR X1, [X0, #0]
8: STUR X1, [X0, #100]

## Slide 17: Hardware Register Renaming (cont.)

## Slide 18: Control Hazards
if (c == 0) { t = s; }
if (a[0] == 0)
a[0] = b[0];
else
a[0] = a[0] + 4;
Branches introduce hazards that limit ILP
  Branch prediction
  Conditional/Predicated instructions

## Slide 19: Predicated Instructions
if (c == 0) { t = s; }
Normal:
W/Conditional move (instructions with internal if-like operation – no branches)
CMOVZ <dest>, <src>, <cond> // move src to dest if cond == 0
CMOVNZ <dest>, <src>, <cond> // move src to dest if cond != 0
Note: ARM actually uses CSEL, a Mux-like instruction instead. But, predication important
enough we’ll pretend there’s a CMOV instruction…

## Slide 20: Predicated Instructions (cont.)
d = a – b;
if (d<0)
sum -= d;
else
sum += d;
Normal:
Predicated Instructions:

## Slide 21: ARM CSEL Instruction: the MUX
CSEL <dest>, <src1>, <src2>, <cond>
<dest> = If <cond> then <src1> else <src2>
<cond>: EQ, NE, LT, etc.
d = a – b;
if (d<0)
sum -= d;
else
sum += d;

## Slide 22: Why ILP
Advanced processors optimize two factors:
Reduce clock period by heavy pipelining
Greater pipelining means more hazards, delay slots
Reduce CPI
What if we want a CPI < 1.0?

## Slide 23: Superpipelining
Divide datapath into multiple pipeline stages
Register
Register
Register
Register
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback
Drive
Alloc
Queue
Exec
Flags
Brnch
Ck
Drive
Pentium 4 Processor (“NetBurst”): 20 stages
TC Nxt IP
TC Fetch
Rename
Schedule
Dispatch
Reg File

## Slide 24: Multiple Issue
Replicate Execution Units
ALU
Shifter
Floating Point
Register File
Memory
Ifetch/Branch
Register
Register
Register
Register
PC
Data
Memory
Instr.
Memory
Register
File
Register
File

## Slide 25: VLIW
Very Long Instruction Word
Max CPI?
Concerns
ALU
ALU
Load/Store
Branch
+
Mem
PC

## Slide 26: VLIW Scheduling
Schedule the code for a 4-way VLIW. Assume no delay slots, and all instructions in parallel with a branch still execute.
ALU1 | ALU2 | Load/Store | Branch
1: LDUR X6, [X0, #4]
2: ADD X7, X6, X0
3: LDUR X8, [X1, #8]
4: SUB X7, X8, X2
5: STUR X10, [X3, #0]
6: CBZ X4, FOO
7: AND X12, X4, X5

## Slide 27: Superscalar
Dynamically schedule multiple instructions, based on hazard detection
Issues
Instr I + 7
+
Mem
PC
Instr I + 6
Instr I + 5
Instr I + 4
Instr I + 3
Instr I + 2
Instr I + 1
Instr I
Schedule/Dispatch
Hazard Detection

## Slide 28: Example Execution on Modern Processors
Bringing everything together, how would this code be run on an advanced CPU? No delay slots, instructions in parallel with a branch still execute
0: LDUR X0, [X1, #8]
1: ADDI X2, X0, #4
2: STUR X2, [X1, #8]
3: CBZ X1, SKIP
4: ADDI X3, X4, #0
SKIP:
5: ADDI X5, X5, #1
6: EORI X0, X1, #5
7: LSL X0, X0, #2
8: STUR X0, [X1, #16]

## Slide 29: Example on VLIW
How would this be scheduled on a 2-way VLIW? Assume no delay slots.
ALU/Load/Store | ALU/Branch

## Slide 30: Example on Superscalar
How would this execute on a 2-way superscalar? Assume it schedules the earliest ready instruction first, and cache miss only stalls dependent instructions.
ALU/Load/Store | ALU/Branch
ALU/Load/Store | ALU/Branch
No miss
2-cycle miss

## Slide 31: Symmetric Multi-Threading (SMT)
~Superscalar drawing from multiple programs or program threads
Issues
+
Mem
PC
Instr L + 7
Instr L + 6
Instr L + 5
Instr L + 4
Instr L + 3
Instr L + 2
Instr L + 1
Instr L
Schedule/Dispatch
Hazard Detection
Instr K + 7
Instr K + 6
Instr K + 5
Instr K + 4
Instr K + 3
Instr K + 2
Instr K + 1
Instr K
Instr J + 7
Instr J + 6
Instr J + 5
Instr J + 4
Instr J + 3
Instr J + 2
Instr J + 1
Instr J
Instr I + 7
Instr I + 6
Instr I + 5
Instr I + 4
Instr I + 3
Instr I + 2
Instr I + 1
Instr I

## Slide 32: Multicore
Add multiple processors (separate control & datapath)
Issues
Processor 1
Computer
Memory
Devices
Input
Output
Processor 2
Processor 3
Processor 4

## Slide 33: Multicore Example
Using a multicore is significantly more complex.
Example: Uniprocessor MAX Multicore MAX
int max(int vals[], int len) {
int result = -infinity;
for (int i=0; i<len; i++) {
if (vals[i] > result)
result = vals[i];
}
return result;
}
int max(int vals[], int len) {
int global_result = -infinity;
int lenT = len/num_procs;
for (int i=0; i<num_proc; i++)
process maxT(&vals[i*lenT], lenT);
}
void maxT(int vals[], int len) {

## Slide 34: Flynn’s Taxonomy
Readings: 6.3, 6.6
Categorize models of parallel computation
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD | SIMD
 | Multiple |  | MIMD
Op
Op
Op
Op

## Slide 35: Early SIMD: Vector Processors
Add vector registers, each holding say 32 ints: V0..V7
Add vector operations. E.g. ADDV V0, V1, V2 // V0i = V1i + V2i
Example: Compute Y = aX+Y. X0 = a, X19 = &X, X20 = &Y
// Vectorized version
LDURV V1, [X19, #0] // Get X
MULVS V2, V1, X0 // a*X
LDURV V3, [X20, #0] // Get Y
ADDV V4, V3, V2 // a*X+Y
STURV V4, [X20, #0] // Save Y
// Standard ARM assembly
ADDI X1, X19, 32*8 // &X[32]
LOOP:
LDUR X2, [X19, #0] // Get X[i]
MUL X2, X2, X1 // a*X[i]
LDUR X3, [X20, #0] // Get Y[i]
ADD X4, X3, X2 // a*X[i]+Y[i]
STUR X4, [X20, #0] // Save Y
ADDI X19, X19, #8 // X++
ADDI X20, X20, #8 // Y++
CMP X1, X19 // X == end?
B.NE LOOP

## Slide 36: Vector Lanes
1 lane 2 lane
Regfile
0, 4, 8, …
Regfile
1, 5, 9, …
Regfile
2, 6, 10, …
Regfile
3, 7, 11, …
A[4]
A[3]
A[2]
A[1]
A[0]
B[4]
B[3]
B[2]
B[1]
B[0]
A[6]
A[4]
A[2]
A[0]
B[6]
B[4]
B[2]
B[0]
A[7]
A[5]
A[3]
A[1]
B[7]
B[5]
B[3]
B[1]

## Slide 37: Vector Considerations
Good:
Repetitive computations
Block-based LDUR/STUR moves (like cache blocks)
Remove loop overhead
Easily parallelized
Bad:
“Jumpy” code: if-then, case
Predicated instructions, but still wasteful
Working on data that isn’t “packed” together.
Scatter/Gather instructions
Can’t accelerate non-vectorized code

## Slide 38: Graphics Processing Units (GPUs)
Processor optimized for graphics processing, coprocessor to main CPU
GPUs, vs. CPUs
CPU coprocessor, so don’t have to support everything.
GPU datasets smaller than CPUs (4-6GB vs. 32-256GB)
Skip multilevel caches, use high-bandwidth memory
Hide latency via multi-threading
Provide many parallel processors (MIMD), that are internally SIMD.
Example
8-16 SIMD Processors
8-16 Lanes/SIMD Processor
Largest cache: 0.75MB (comparable CPU might be 8MB)
DRAM: 4-6GB (comparable CPU might be 8-256GB)

## Slide 39: GPU SIMD Processor