## Slide 1: Pipelining
Readings: 4.5-4.8
Example: Doing the laundry
Ann, Brian, Cathy, & Dave
each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 2: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 3: Pipelined Laundry: Start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 4: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
Stall for Dependences
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 5: Pipelined Execution
Now we just have to make it work
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
Program Flow
Time

## Slide 6: Single Cycle vs. Pipeline
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Load
Ifetch
Reg
Exec
Mem
Wr
Pipeline Implementation:
Ifetch
Reg
Exec
Mem
Wr
Store
Clk
Single Cycle Implementation:
Load
Store
Waste
Ifetch
Reg
Exec
Mem
Wr
R-type
Cycle 1
Cycle 2

## Slide 7: Why Pipeline?
Suppose we execute 100 instructions
Single Cycle Machine
  45 ns/cycle x 1 CPI x 100 inst = ____ ns
Ideal pipelined machine
  10 ns/cycle x (1 CPI x 100 inst + 4 cycle drain) = ____ ns

## Slide 8: CPI for Pipelined Processors
Ideal pipelined machine
  10 ns/cycle x (1 CPI x 100 inst + 4 cycle drain) = ____ ns
CPI in pipelined processor is “issue rate”. Ignore fill/drain, ignore latency.
Example: A processor wastes 2 cycles after every branch, and 1 after every load, during which it cannot issue a new instruction. If a program has 10% branches and 30% loads, what is the CPI on this program?

## Slide 9: Pipelined Datapath
Register
Register
Register
Register
Divide datapath into multiple pipeline stages
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback

## Slide 10: Pipelined Control
The Main Control generates the control signals during Reg/Dec
  Control signals for Exec (ALUOp, ALUSrc, …) are used 1 cycle later
  Control signals for Mem (MemWE, Mem2Reg, …) are used 2 cycles later
  Control signals for Wr (RegWE, …) are used 3 cycles later
IF/ID Register
ID/Ex Register
Ex/Mem Register
Mem/Wr Register
Reg/Dec
Exec
Mem
Main
Control
ALUSrc
ALUSrc
ALUOp
ALUOp
RegWE
RegWE
RegWE
RegWE
MemWE
MemWE
MemWE
Mem2Reg
Mem2Reg
Mem2Reg
Wr

## Slide 11: Can pipelining get us into trouble?
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource two different ways at the same time
    E.g., combined washer/dryer would be a structural hazard or folder busy doing something else (watching TV)
  data hazards: attempt to use item before it is ready
    E.g., one sock of pair in dryer and one in washer; can’t fold until get sock from washer through dryer
    instruction depends on result of prior instruction still in the pipeline
  control hazards: attempt to make decision before condition evaluated
    E.g., washing football uniforms and need to get proper detergent level; need to see after dryer before next load in
    branch instructions
Can always resolve hazards by waiting
  pipeline control must detect the hazard
  take action (or delay action) to resolve hazards

## Slide 12: Pipelining the Load Instruction
The five independent functional units in the pipeline datapath are:
  Instruction Memory for the Ifetch stage
  Register File’s Read ports (bus A and busB) for the Reg/Dec stage
  ALU for the Exec stage
  Data Memory for the Mem stage
  Register File’s Write port (bus W) for the Wr stage
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Ifetch
Reg/Dec
Exec
Mem
Wr
1st LDUR
Ifetch
Reg/Dec
Exec
Mem
Wr
2nd LDUR
Ifetch
Reg/Dec
Exec
Mem
Wr
3rd LDUR

## Slide 13: The Four Stages of R-type
Ifetch: Fetch the instruction from the Instruction Memory
Reg/Dec: Register Fetch and Instruction Decode
Exec: ALU operates on the two register operands
Wr: Write the ALU output back to the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Wr
R-type

## Slide 14: Structural Hazard
Interaction between R-type and loads causes structural hazard on writeback
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type

## Slide 15: Important Observation
Each functional unit can only be used once per instruction
Each functional unit must be used at the same stage for all instructions:
  Load uses Register File’s Write Port during its 5th stage
  R-type uses Register File’s Write Port during its 4th stage
Solution: Delay R-type’s register write by one cycle:
  Now R-type instructions also use Reg File’s write port at Stage 5
  Mem stage is a NOOP stage: nothing is being done.
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
1
2
3
4
5
Ifetch
Reg/Dec
Exec
Wr
R-type
1
2
3
4
Ifetch
Reg/Dec
Exec
Wr
R-type
Mem
1
2
3
4
5

## Slide 16: Pipelining the R-type Instruction
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec

## Slide 17: The Four Stages of Store
Ifetch: Fetch the instruction from the Instruction Memory
Reg/Dec: Register Fetch and Instruction Decode
Exec: Calculate the memory address
Mem: Write the data into the Data Memory
Wr: NOOP
Compatible with Load & R-type instructions
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Mem
Store
Wr

## Slide 18: The Stages of Conditional Branch
Ifetch: Fetch the instruction from the Instruction Memory
Reg/Dec: Register Fetch and Instruction Decode, compute branch target
Exec: Test condition & update the PC
Mem: NOOP
Wr: NOOP
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Mem
Beq
Wr

## Slide 19: Control Hazard
Branch updates the PC at the end of the Exec stage.
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
CBZ
Ifetch
Reg/Dec
Exec
Mem
Wr
load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec

## Slide 20: Accelerate Branches
Register
Register
Register
Register
When can we compute branch target address?
When can we compute the CBZ condition?
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback

## Slide 21: Control Hazard 2
Branch updates the PC at the end of the Reg/Dec stage.
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
CBZ
Ifetch
Reg/Dec
Exec
Mem
Wr
load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Mem
CBZ
Wr

## Slide 22: Solution #1: Stall
Delay loading next instruction, load no-op instead
CPI if all other instructions take 1 cycle, and branches are 20% of instructions?
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
CBZ
Ifetch
Reg/Dec
Exec
Mem
Wr
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec
Bubble
Bubble
Bubble
Bubble
Stall

## Slide 23: Solution #2: Branch Prediction
Guess all branches not taken, squash if wrong
CPI if 50% of branches actually not taken, and branch frequency 20%?
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
CBZ
Ifetch
Reg/Dec
Exec
Mem
Wr
load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec

## Slide 24: Solution #3: Branch Delay Slot
Redefine branches: Instruction directly after branch always executed
Instruction after branch is the delay slot
Compiler/assembler fills the delay slot
ADD X1, X0, X4
CBZ X2, FOO
SUB X2, X0, X3
ADD X1, X0, X4
CBZ X1, FOO
ADD X1, X0, X4
CBZ X1, FOO
ADD X1, X3, X3
…
FOO:
ADD X1, X2, X0
ADD X1, X0, X4
CBZ X1, FOO

## Slide 25: Data Hazards
Consider the following code:
  ADD X0, X1, X2
  SUB X3, X0, X4
  AND X5, X0, X6
  ORR X7, X0, X8
  EOR X9, X0, X10
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
ADD
Ifetch
Reg/Dec
Mem
SUB
Ifetch
Reg/Dec
Exec
Wr
AND
Ifetch
Reg/Dec
Mem
Wr
ORR
Ifetch
Reg/Dec
Mem
Wr
EOR
Exec
Exec
Exec

## Slide 26: Design Register File Carefully
What if reads see value after write during the same cycle?
  ADD X0, X1, X2
  SUB X3, X0, X4
  AND X5, X0, X6
  ORR X7, X0, X8
  EOR X9, X0, X10
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
ADD
Ifetch
Reg/Dec
Mem
SUB
Ifetch
Reg/Dec
Exec
Wr
AND
Ifetch
Reg/Dec
Mem
Wr
ORR
Ifetch
Reg/Dec
Mem
Wr
EOR
Exec
Exec
Exec

## Slide 27: Forwarding
Add logic to pass last two values from ALU output to ALU input(s) as needed
  Forward the ALU output to later instructions
  ADD X0, X1, X2
  SUB X3, X0, X4
  AND X5, X0, X6
  ORR X7, X0, X8
  EOR X9, X0, X10
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
ADD
Ifetch
Reg/Dec
Mem
SUB
Ifetch
Reg/Dec
Exec
Wr
AND
Ifetch
Reg/Dec
Mem
Wr
ORR
Ifetch
Reg/Dec
Mem
Wr
EOR
Exec
Exec
Exec

## Slide 28: Forwarding (cont.)
Register
Register
Register
Register
Requires values from last two ALU operations.
Remember destination register for operation.
Compare sources of current instruction to destinations of previous 2.
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback

## Slide 29: Data Hazards on Loads
  LDUR X0, [X31, 0]
  SUB X3, X0, X4
  AND X5, X0, X6
  ORR X7, X0, X8
  EOR X9, X0, X10
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
LDUR
Ifetch
Reg/Dec
Mem
SUB
Ifetch
Reg/Dec
Exec
Wr
AND
Ifetch
Reg/Dec
Mem
Wr
ORR
Ifetch
Reg/Dec
Mem
Wr
EOR
Exec
Exec
Exec

## Slide 30: Data Hazards on Loads (cont.)
Solution:
  Use same forwarding hardware & register file for hazards 2+ cycles later
  Force compiler to not allow register reads within a cycle of load
    Fill delay slot, or insert no-op.

## Slide 31: Pipelined CPI, cycle time
CPI, assuming compiler can fill 50% of delay slots
Pipelined: cycle time = 1ns. Delay for 1M instr:
Single cycle: CPI = 1.0, cycle time = 4.5ns. Delay for 1M instr:
Instruction Type | Type Cycles | Type Frequency | Cycles * Freq
ALU |  | 50% | 
Load |  | 20% | 
Store |  | 10% | 
Branch |  | 20% | 
 |  | CPI: | 

## Slide 32: Pipelined CPU Summary